## Slide 1: Embedded GarageBand
By: Maulik Kapuria
Niket Shah
Vishal Verma
ECEN-5613
Embedded System Design
Spring 2011

## Slide 2: Project Overview
Instruments played are: Piano, Guitar and Drums.
Play MIDI notes using “Real” Instruments and “Virtual” Instruments.
Virtual: They are the instruments created using graphics LCD and touch screen.
Real : They are the instruments that are made using keyboard & piezo buzzers.
Gives the option to select what type of instrument(drum, guitar etc) to play. Also provides an option to select the subtype of a particular instrument (Acoustic Piano, Electric Piano etc)
Record & playback the Notes using an I2C EEPROM.
27th April 2011

## Slide 3: Very High Level Block Diagram
27th April 2011
Components & Interfaces
Control & Data Lines
Wireless Communication
Components & Interfaces
Control & Data Lines
This kind of system was selected since it distributed the strain on peripherals.
The tradeoff was made between
  Adding a complex RF communication interface &
  Simplifying the design
CC2430
Module 2
CC2430
Module 1

## Slide 4: Block Diagram
Note: Components like Oscillator & Reset Circuit are not shown here
Graphic LCD
128x64 LED Backlight
4-wire
Touch
Screen
Serial Interface to Computer
Virtual Instrument Pressure Piezo
Heart Beat LED
Analog
Analog
GPIO
Serial
Serial
CC2430
Module 1
Piezo 1
Piezo 2
Piezo 3
Piezo 4
Piezo 5
VS1053 MIDI Decoder
Comparator
HeartBeat LED
2 Wire EEPROM
Reference Generator
CC2430
Module 2
Real Time MIDI Serial
RF
RF
I2C
GPIO
Int & Timers
27th April 2011

## Slide 5
© http://attemptcreativity.blogspot.com/
27th April 2011